## Slide 1: Image-Based Situation Awareness Audit 1.3.2018
Sakari Lampola

## Slide 2: Previous Audit 11.1.2018

## Slide 3
Previous Audit
Open questions:
Role of classical object tracking alrorithms?
What to do with multiple bounding boxes around one object?
Appropriate minimum confidence level?
What to do with false detections inside other objects?
What to do with false detections from the background?
How to set Kalman filter parameters for image object filtering?
Hungarian algorithms special case for hidden objects
To do:
Close open questions
Image object status
Image object velocity estimation
Probabilistic approach for matching detected and image objects
2d -> 3d transformation
World object state estimation
Other:
Semantic segmentation
Organisations to follow: ICCV, ICRA, NIPS, IROS, arXiv
Camera motion (yaw, pitch)
Grid or continuos presentation?
Class specific attributes
Object history

## Slide 4: Project Plan

## Slide 5
Project Plan
Methodology / Preparation of research infra
  Software platforms are constructed and tested
  Off-the-shelf models are acquired and tested
  Necessary skills on platforms are learned
Methodology / Method survey
  Current state-of-art methods are studied
  Methods are constructed and tested on the software platforms
Method follow-up
  Screening of conference papers related to the subject
  Possibly integrating new methods to the project

## Slide 6: Work Done

## Slide 7
Method Follow-Up

## Slide 8
Image Object Velocity Estimation
Image object velocity is necessary for:
predicting image object locations when matching new measurements
identifying image objects
predicting image object locations for hidden objects
Image object
  id
  status
  x_min
  x_max
  y_min
  y_max
  vx_min
  vx_max
  vy_min
  vy_max
  class
  confidence
  appearance
Estimation algorithm
Numerical values are estimated using grid search and 10 step ahead
mean prediction error. Values rounded. Later adjusted by experiments.

## Slide 9
Image Object Velocity Estimation
Moving object (car)
Measured and filtered location (upper left corner)
Estimated velocity
Location variance
Velocity variance

## Slide 10
Image Object Velocity Estimation
Moving object (car)
10 step ahead mean prediction error

## Slide 11
Image Object Velocity Estimation
Static object (calf)
Measured and filtered location (upper left corner)
Estimated velocity
Location variance
Velocity variance

## Slide 12
Image Object Velocity Estimation
10 step ahead mean prediction error
Static object (calf)

## Slide 13
Speech Synthesis
Software Architecture
OpenCV
AnalyzeVideo
Video file
Camera
ObjectDetection
MobileNetSSD (caffe)
ImageClasses
pyttsx3
SpeechSynthesis
Speakers

## Slide 14
Speech Synthesis
Entities
Image World
Image Object
Event
Event
time
text
priority
Event is generated when
  new image object is created
  image object status is changed
Event will pause the video for the duration of speech (not in the final version)
Events are collected (history)

## Slide 15
Confidence Level
SSD Mobilenet implementation:
# extract the confidence (i.e., probability) associated with the prediction
Good value for creating a new image object is between 0.8 and 0.9.
The ’good’ value also depends on other hyperparameters.

## Slide 16
Confidence Level
Update (not class)
create
Different levels for creating and updating image object. Hyperparameters:
CONFIDENCE_LEVEL_CREATE (0.8)
CONFIDENCE_LEVEL_UPDATE (0.2)
Confidence level has dynamics
ignore

## Slide 17
Confidence Level

## Slide 18
Border Behaviour
Box size and form distorded
Hyperparameter BORDER_WIDTH (30)

## Slide 19
Border Behaviour
1
2
4
3
6
5
Type 3 and 5: world object not updated
Type 6: removed, world object acceleration fixed
If an object touches 3 borders, it is removed
Done for:
left
right
top
bottom

## Slide 20
Visual Presentation
Ellipse axes proportional to the standard deviation of the location (2*std, corresponding to 95% probability)
Arrow direction and length proportional to velocity (measured in pixels/second)

## Slide 21
Object Retention
Image objects are removed if not detected in RETENTION_COUNT_MAX (30) successive frames.

## Slide 22
Distance Estimation
f
A
B
C
D
E
h
hi
Similar triangles AGE and AFD:
α
F
G
AF=d (distance)
Simalar equations for horizontal direction
(β=azimuth)

## Slide 23
Distance Estimation
sw
sh
pw= image width (pixels)
ph= image height (pixels)
hi = object height (pixels)
h = object height (m)
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
Example (Nikon D800E):
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  hi = object height (pixels) = 100
  h = object height (m) = 1.0 m
  f = focal length (m) = 0.050 m
  = altitude (rad) = 0.0
  β = azimuth (rad) = 0.0

## Slide 24
2d -> 3d Transformation
From pixel coordinates (sensor plane) to 3d camera coordinates:
(xc, yc, zc) = (- * , * , -f)
x
z
y
Object center will be on the line:
(xo, yo, zo) = t* (xc, yc, zc)
The length of the line is:
sw
sh
pw= image width (pixels)
ph= image height (pixels)
hi = object height (pixels)
h = object height (m)
f = focal length (m)
= altitude (rad)
arc tan(yc/f)
arc tan(xc/f)

## Slide 25
2d -> 3d Transformation

## Slide 26
2d -> 3d Transformation
Example:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  hi = object height (pixels) = 100
  h = object height (m) = 1.0 m
  f = focal length (m) = 0.050 m
  xp = 1200
  yp = 2000
(xc, yc, zc) = (- * , * , -f)
= (- * , * , -0.050)
= (-0.0121, 0.0022, -0.0500)
arc tan(yc/f) = 0.0445
arc tan(xc/f) = -0.2374
= 105.39
= 2.0468e+03

## Slide 27
2d -> 3d Transformation
(xo, yo, zo) = t* (xc, yc, zc)
Object location in 3d camera coordinates:
= 2.0468e+03 * (-0.0121, 0.0022, -0.0500)
(-24.7593, 4.5602, -102.3389)
Open questions:
Derivation ok?
Assumptions ok?
  Optical axis in sensor center?

## Slide 28
2d -> 3d Transformation
Parameters:
  sw
  sh
  pw= image width (pixels)
  ph= image height (pixels)
  f = focal length (m)
Open questions:
Video metadata often lacks sensor and focal parameters
Focal length can change during shooting (zooming)

## Slide 29
Map Presentation
z
x
image x - coordinate
image y – coordinate
field of view
object
observer
xw
zw
xi
yi
hw= image area world height (m)
hi = image area image height (pixels)
ww= image area world width (m)
wi = image area image width (pixels)
(xi, yi) = ( w* , * )
= = p (pixel/meter ratio)
(xi, yi) = ( w* , *p)

## Slide 30
Map Presentation
z
x
image x - coordinate
image y – coordinate
field of view
object
observer
sw
f = focal length (m)

## Slide 31: Work in Progress

## Slide 32
Perception
“The first step in achieving SA is to perceive the status, attributes, and dynamics of relevant elements in the environment. Thus, Level 1 SA, the most basic level of SA, involves the processes of monitoring, cue detection, and simple recognition, which lead to an awareness of multiple situational elements (objects, events, people, systems, environmental factors) and their current states (locations, conditions, modes, actions).”

## Slide 33: Next Steps

## Slide 34
Next steps
Comprehension:
Closing the open questions
2d -> 3d transformation
World object state estimation

## Slide 35: To Be Discussed

## Slide 36
To Be Discussed
Activity recognition?
Emotion recognition?
Turning camera, estimation by background movement?

## Slide 37: Thank you!
lampola@student.tut.fi
https://github.com/SakariLampola/Thesis