## Slide 1: Image-Based Situation Awareness Audit 28.2.2018
Sakari Lampola

## Slide 2: Previous Audit 11.1.2018

## Slide 3
Previous Audit
Open questions:
Role of classical object tracking alrorithms?
What to do with multiple bounding boxes around one object?
Appropriate minimum confidence level?
What to do with false detections inside other objects?
What to do with false detections from the background?
How to set Kalman filter parameters for image object filtering?
Hungarian algorithm, special case for hidden objects
To do:
Close open questions
Image object status
Image object velocity estimation
Probabilistic approach for matching detected and image objects
2d -> 3d transformation
World object state estimation
Other:
Semantic segmentation
Organisations to follow: ICCV, ICRA, NIPS, IROS, arXiv
Camera motion (yaw, pitch,roll)
Grid or continuos presentation?
Class specific attributes
Object history

## Slide 4: Project Plan

## Slide 5
Project Plan
Methodology / Preparation of research infra
  Software platforms are constructed and tested
  Off-the-shelf models are acquired and tested
  Necessary skills on platforms are learned
Methodology / Method survey
  Current state-of-art methods are studied
  Methods are constructed and tested on the software platforms
Method follow-up
  Screening of conference papers related to the subject
  Possibly integrating new methods to the project

## Slide 6: Work Done

## Slide 7
Method Follow-Up

## Slide 8
Method Survey
Christoffer Manning & Richard Socher

## Slide 9
Method Survey
Goodfellow, Bengio, Courville: Deep Learning

## Slide 10
Software Version 2.0
V2.0 Goal
Detected classes not hardcoded
Object class may change
Support for many cameras , rotations, movement
Names less awkward, terminology fixed
Cleaning
Python style guide followed, excluding line length
Code optimization
One package
Language (speech synthesizer)
Name of the software package: ShadowWorld
(Plato: Allegory of the Cave)

## Slide 11
Software Version 2.0
Detection
Pattern
Event
World
Class Diagram
Camera
Body
”World object”
”Image object”
”Detected object”
Trace
Speech
Synthesizer
PresentationForecast
Presentation
…
PresentationMap
Bounding
Box
PresentationLog
Forecast

## Slide 12
Software Version 2.0
Detection
Matching
Pattern Filtering
3D Projection
Body Filtering
Body Prediction
Distance Estimation
Collision Detection

## Slide 13
Software Version 2.0
Language
Event
time
priority
text
(object)
Speech synthesizer based on pyttsx3 package
Event is spelled out if priority <= 0
Event will pause video for the duration of speech (to be changed later by using separate thread)
Example events:
  Body observed (1 sec after created)
  Collision warning
Speech recognition later
pyttsx3
Event
World
Speech
Synthesizer

## Slide 14
Software Version 2.0
detection
Visual Presentation (pattern)
bounding box
bounding circle
center point
class
confidence
center point confidence (ellipse, axes=2*standard deviation)
center point velocity (pixels/sec)

## Slide 15
Software Version 2.0
Visual Presentation (body)
body (green, with reliable pattern)
body (red, with unreliable or lost pattern)
field of camera view
distance circles (every 10m)
location uncertainty (ellipse, axes = standard deviation)
body size (circle, radius = mean class specific radius)
observer (+camera)

## Slide 16
Software Version 2.0
Visual Presentation (forecast)
body size (circle, radius = mean class specific radius)
Forecast made every FORECAST_INTERVAL (=1.0) seconds
body location, when forecast was made
body location, current
body location predicted path
body location after FORECAST_COUNT*FORECAST_DELTA seconds
observer
collision probability > 1

## Slide 17
Software Version 2.0
Logging

## Slide 18
Software Version 2.0
Demo
  3-5 videos
  Short program code review
How to use?

## Slide 19
Pattern Filtering
Why pattern filtering?
Reduces object detection noise (bounding box)
Provides prediction for pattern location in the next frame - matching easier
Predicts pattern location when detection is missing
Hyperparameters:

## Slide 20
Pattern Filtering

## Slide 21
Pattern Filtering

## Slide 22
Pattern Filtering
Matched status, coordinate and velocity

## Slide 23
Pattern Filtering
Covariance matrix
0=location, 1=velocity

## Slide 24
Matching / Confidence Level
Good value for creating a new pattern is between 0.8 and 0.9.
Minimum confidence level to create a pattern (and body) was varied between 0 and 1. The number of bodies created was compared to
the true number of objects in the video.

## Slide 25
Matching / Confidence Level
update
create
Different levels for creating and updating image object.
Hyperparameters:
CONFIDENCE_LEVEL_CREATE (0.8)
CONFIDENCE_LEVEL_UPDATE (0.2)
Confidence level has dynamics
ignore

## Slide 26
Matching / Border Behaviour
The problem: Bounding box size and form are distorded near edges
Hyperparameter BORDER_WIDTH (30)

## Slide 27
Matching / Border Behaviour
1
2
4
3
6
5
If a pattern touches 3 borders, it is removed
Reliable = body information updated
Done for:
left
right
top
bottom
Reliable
Reliable
Unreliable
Reliable, not created
Unreliable, not created
Unreliable, removed

## Slide 28
Matching / Pattern Retention
Patterns are removed if not detected in RETENTION_COUNT_MAX (30) successive frames.

## Slide 29
Distance Estimation
f
A
B
C
D
E
h
hi
Similar triangles AGE and AFD:
α
F
G
d (distance)=AF

## Slide 30
Distance Estimation
sw
sh
pw= image width (pixels)
ph= image height (pixels)
li = object length (pixels)
l = object length (m)
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
Example (Nikon D800E):
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  hi = object height (pixels) = 100
  h = object height (m) = 1.0 m
  f = focal length (m) = 0.050 m
  = altitude (rad) = 0.0
  β = azimuth (rad) = 0.0
Similar equations for horizontal direction (β=azimuth):
Assumptions:
equal vertical/horizontal pixel spacing
optical axis in image center

## Slide 31
Distance Estimation
Question: How to compare pattern and body sizes for distance estimation?
Height or width alone might be misleading.
Some form of (3D) spatial simplification is needed, like
cube
rectangular prism
cylinder
sphere (probably the easiest math)
Uncertainty should be modeled.
Solution:
pattern circle <---> body sphere

## Slide 32
Distance Estimation
Body radius distribution
Distibution should
  be defined in [0,∞]
  mode > 0
  simple
  skew controllable

## Slide 33
Distance Estimation
Log-normal distribution for body radius
Used in the context of describing human height distribution

## Slide 34
Distance Estimation
Example: Person

## Slide 35
Distance Estimation
Bubble diameters (2*radius)

## Slide 36
Distance Estimation
Bubble diameters (2*radius)

## Slide 37
Distance Estimation
Bubble diameters (2*radius)

## Slide 38
Distance Estimation
Bubble diameters (2*radius)

## Slide 39
Distance Estimation
Bubble diameters (2*radius)

## Slide 40
Distance Estimation
Radius of enclosing circle will be used for pattern
h
w
r
α
From bounding box coordinates to radius:
/2

## Slide 41
Distance Estimation
Distance estimation using pattern circle and body sphere
sh
ph= image height (pixels)
ri = pattern radius (pixels)
r = body radius (m), mean from class specific distribution
f = focal length (m)
= altitude (rad)
β = azimuth (rad)

## Slide 42
Distance Estimation
Remarks:
Video metadata often lacks sensor and focal parameters
Focal length can change during shooting (zooming)

## Slide 43
3D Projection
From pixel coordinates xp, yp (sensor plane) to 3d camera coordinates:
(xp, yp, zp) = (- * , * , -f)
x
z
y
Body center will be on the line:
(xb, yb, zb) = t* (xp, yp, zp)
The distance to the body is:
sw
sh
pw= image width (pixels)
ph= image height (pixels)
hi = object height (pixels)
h = object height (m)
f = focal length (m)
= altitude (rad)
arc tan(yp/f)
arc tan(xp/f)
xb,yb,zb = body center point
xp,yp,zp = pattern center point

## Slide 44
3D Projection
So:
Solving for t:
(xb, yb, zb) = t* (xp, yp, zp)
(xp, yp, zp) = (- * , * , -f)
Where:

## Slide 45
3D Projection
Example:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  ri = pattern radius (pixels) = 100
  r = body radius (m) = 1.0 m
  f = focal length (m) = 0.050 m
  xp = 1200
  yp = 2000
(xp, yp, zp) = (- * , * , -f)
= (- * , * , -0.050)
= (-0.0121, 0.0022, -0.0500)
arc tan(yp/f) = 0.0445
arc tan(xp/f) = -0.2374
= 105.39
(xb, yb, zb) = t* (xp, yp, zp)
= 2.0468e+03 * (-0.0121, 0.0022, -0.0500)
= (-24.7593, 4.5602, -102.3389)
= 2.0468e+03

## Slide 46
Body Filtering
General
Enables prediction, including collision detection
Second order model does not work, constant acceleration makes bodies bounce back or get enormous velocities
In world, constant acceleration for several (tens) of seconds is not common
First order model works! (No wonder it’s popular in robotics…)
When measurement is lost, the body is switched into constant velocity mode

## Slide 47
Body Filtering

## Slide 48
Body Filtering

## Slide 49
Body Filtering

## Slide 50
Body Filtering
Example 1

## Slide 51
Body Filtering

## Slide 52
Body Filtering

## Slide 53
Body Filtering
Example 2

## Slide 54
Body Filtering

## Slide 55
Body Filtering

## Slide 56
Body Prediction
Path chosen - a simpler solution which provides a lot more information
A
μ
∆ has to be smaller than 1/fps. If fps=25, 1/fps = 0.04 sec. A car driving 120 km/h will proceed
1.33 meters and a collision with an observer might not be detected well enough. A value of ∆ = 0.01 corresponds to the movement of 33 cm for an object moving at 120 km/h. This will generate 100 predictions per second. If we want the prediction horizon to be 10 secs, we have
1000 predictions per object. Predicting for every frame will generate fps*1000 ≈ 25 000 predictions per second per object. This is too much, so only current prediction is saved. Prediction is also done only once per second.

## Slide 57
Body Prediction

## Slide 58
Collision Detection
Collision with the observer
nearest point μi on the predicted trajectory
t=t’
filter covariance estimate Vi
d
O
ri
r
Collisions
For each body i, a random vector t is sampled
and distance to the observer calculated (center to center).
If the distance is less than ri+r, collision occurred. The proportion of collisions to all cases is the (maximum) probability estimate for the body/observer collision.
μi
From Kalman filter
Class specific
m=1000
Note! Collision might occur earlier. This algorithm estimates the maximum probability on the path. Should minimum time used? Or both?

## Slide 59
Collision Detection
Example

## Slide 60
Collision Detection
Open questions:
  Collisions between all bodies?
  Min time or max probability or both?
  More efficient sampling?
Note:
Min distance and corresponding
time can be calculated without
step by step prediction

## Slide 61: The Big Picture

## Slide 62
Situation Analysis
Captioning
Question Answering
Bodies (+attributes)
Forecasts
Collision probabilities
Other representations
Captions
Answers
Language Composition
Words per minute:
150…160
+ Description
Priority queue
Transfer learning?

## Slide 63: Next Steps

## Slide 64
Next steps
Kalman filter parameter adjustments
Dataset selection
Stereo vision
Camera yaw, pitch, roll estimation
Semantic segmentation
Experiments in the wild
Paper
Visual captioning
Visual question answering
Language composition

## Slide 65
Kalman Filter Parameter Adjustments

## Slide 66
Kalman Filter Parameter Adjustments

## Slide 67
Dataset Selection
Specification (situation analysis):
  Video
  Stereo
  Distance information
  Outdoor + indoor
  Odometry

## Slide 68
Stereo Vision
Left
Right
Disparity for “free” using left and right bounding boxes!!!!!!!!!!
If this works, stereo algorithm will be extremely fast and easy….

## Slide 69
Camera yaw, pitch, roll estimation
Can be estimated from background movement (average
optical flow)?

## Slide 70
Semantic Segmentation
Why?
  Object context (street, forest, …)
  More exact localization
Which off-the-shelf network to use? Must be light and fast.

## Slide 71
Experiments In Wild
Location calculation
Nikon D800E:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  h = object height (m) = 1.5 m
  f = focal length (m) = 0.020 m
  fov = = 83.81 ⁰
Different locations and heights

## Slide 72
Experiments In Wild
Velocities (moving car)
Nikon D800E:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  h = object height (m) = 1.5 m
  f = focal length (m) = 0.050 m
  fov = = 39.49 ⁰
Car speeds:
  0
  20 km/h
  40 km/h
  60 km/h
  80 km/h
Distances:
  10 m
  20 m
  30 m
  40 m
  50 m
  60 m
  70 m
  80 m
  90 m
  100 m

## Slide 73
Paper
Contents:
Abstract
Introduction
Related work
Our approach
  Definitions
  Detection
  Matching
  Pattern Filtering
  Distance Estimation
  3D Projection
  Body Filtering
  Body Prediction
  Collision Detection
Experiments
  Evaluation metric
  Dataset
  Results
  Other experiments
Conclusion
Image-Based Situation Awareness: Estimating Object Locations, Velocities and Collision Probabilities Using Object Detection

## Slide 74
Paper
Where to publish?
  CVPR 2019 (6/2019, Long Beach, deadline 11/2018)
  ICCV 2019 (29.10.-3.11.2019, Seoul, deadline 1/2019)

## Slide 75
Visual Captioning
Which off-the-shelf network to use? Must be light and fast.
Transfer learning should be possible.
Which dataset?

## Slide 76
Visual Question Answering
Which off-the-shelf network to use? Must be light and fast.
Transfer learning should be possible.
Which dataset?

## Slide 77
Language Composition
?

## Slide 78: Discussion

## Slide 79
Discussion
Activity recognition?
Emotion recognition?

## Slide 80: Thank you!
lampola@student.tut.fi
https://github.com/SakariLampola/Thesis