## Slide 1: Image-Based Situation Awareness Audit 28.2.2018
Sakari Lampola

## Slide 2: Previous Audit 11.1.2018

## Slide 3
Previous Audit
Open questions:
Role of classical object tracking alrorithms?
What to do with multiple bounding boxes around one object?
Appropriate minimum confidence level?
What to do with false detections inside other objects?
What to do with false detections from the background?
How to set Kalman filter parameters for image object filtering?
Hungarian algorithms special case for hidden objects
To do:
Close open questions
Image object status
Image object velocity estimation
Probabilistic approach for matching detected and image objects
2d -> 3d transformation
World object state estimation
Other:
Semantic segmentation
Organisations to follow: ICCV, ICRA, NIPS, IROS, arXiv
Camera motion (yaw, pitch)
Grid or continuos presentation?
Class specific attributes
Object history

## Slide 4: Project Plan

## Slide 5
Project Plan
Methodology / Preparation of research infra
  Software platforms are constructed and tested
  Off-the-shelf models are acquired and tested
  Necessary skills on platforms are learned
Methodology / Method survey
  Current state-of-art methods are studied
  Methods are constructed and tested on the software platforms
Method follow-up
  Screening of conference papers related to the subject
  Possibly integrating new methods to the project

## Slide 6: Work Done

## Slide 7
Method Follow-Up

## Slide 8
Image Object Velocity Estimation
Image object velocity is necessary for:
predicting image object locations when matching new measurements
identifying image objects
predicting image object locations for hidden objects
Image object
  id
  status
  x_min
  x_max
  y_min
  y_max
  vx_min
  vx_max
  vy_min
  vy_max
  class
  confidence
  appearance
Estimation algorithm
Numerical values are estimated using grid search and 10 step ahead
mean prediction error. Values rounded. Later adjusted by experiments.

## Slide 9
Image Object Velocity Estimation
Moving object (car)
Measured and filtered location (upper left corner)
Estimated velocity
Location variance
Velocity variance

## Slide 10
Image Object Velocity Estimation
Moving object (car)
10 step ahead mean prediction error

## Slide 11
Image Object Velocity Estimation
Static object (calf)
Measured and filtered location (upper left corner)
Estimated velocity
Location variance
Velocity variance

## Slide 12
Image Object Velocity Estimation
10 step ahead mean prediction error
Static object (calf)

## Slide 13
Speech Synthesis
Software Architecture
OpenCV
AnalyzeVideo
Video file
Camera
ObjectDetection
MobileNetSSD (caffe)
ImageClasses
pyttsx3
SpeechSynthesis
Speakers

## Slide 14
Speech Synthesis
Entities
Image World
Image Object
Event
Event
time
text
priority
Event is generated when
  new image object is created
  image object status is changed
Event will pause the video for the duration of speech (not in the final version)
Events are collected (history)

## Slide 15
Confidence Level
SSD Mobilenet implementation:
# extract the confidence (i.e., probability) associated with the prediction
Good value for creating a new image object is between 0.8 and 0.9.
The ’good’ value also depends on other hyperparameters.

## Slide 16
Confidence Level
Update (not class)
create
Different levels for creating and updating image object. Hyperparameters:
CONFIDENCE_LEVEL_CREATE (0.8)
CONFIDENCE_LEVEL_UPDATE (0.2)
Confidence level has dynamics
ignore

## Slide 17
Confidence Level

## Slide 18
Border Behaviour
Box size and form distorded
Hyperparameter BORDER_WIDTH (30)

## Slide 19
Border Behaviour
1
2
4
3
6
5
Type 3 and 5: world object not updated
Type 6: removed, world object acceleration fixed
If an object touches 3 borders, it is removed
Done for:
left
right
top
bottom

## Slide 20
Visual Presentation
Ellipse axes proportional to the standard deviation of the location (2*std, corresponding to 95% probability)
Arrow direction and length proportional to velocity (measured in pixels/second)

## Slide 21
Object Retention
Image objects are removed if not detected in RETENTION_COUNT_MAX (30) successive frames.

## Slide 22
Distance Estimation
f
A
B
C
D
E
h
hi
Similar triangles AGE and AFD:
α
F
G
AF=d (distance)
Similar equations for horizontal direction
(β=azimuth)

## Slide 23
Distance Estimation
sw
sh
pw= image width (pixels)
ph= image height (pixels)
hi = object height (pixels)
h = object height (m)
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
Example (Nikon D800E):
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  hi = object height (pixels) = 100
  h = object height (m) = 1.0 m
  f = focal length (m) = 0.050 m
  = altitude (rad) = 0.0
  β = azimuth (rad) = 0.0

## Slide 24
2d -> 3d Transformation
From pixel coordinates (sensor plane) to 3d camera coordinates:
(xc, yc, zc) = (- * , * , -f)
x
z
y
Object center will be on the line:
(xo, yo, zo) = t* (xc, yc, zc)
The length of the line is:
sw
sh
pw= image width (pixels)
ph= image height (pixels)
hi = object height (pixels)
h = object height (m)
f = focal length (m)
= altitude (rad)
arc tan(yc/f)
arc tan(xc/f)

## Slide 25
2d -> 3d Transformation

## Slide 26
2d -> 3d Transformation
Example:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  hi = object height (pixels) = 100
  h = object height (m) = 1.0 m
  f = focal length (m) = 0.050 m
  xp = 1200
  yp = 2000
(xc, yc, zc) = (- * , * , -f)
= (- * , * , -0.050)
= (-0.0121, 0.0022, -0.0500)
arc tan(yc/f) = 0.0445
arc tan(xc/f) = -0.2374
= 105.39
= 2.0468e+03

## Slide 27
2d -> 3d Transformation
(xo, yo, zo) = t* (xc, yc, zc)
Object location in 3d camera coordinates:
= 2.0468e+03 * (-0.0121, 0.0022, -0.0500)
(-24.7593, 4.5602, -102.3389)
Open questions:
Derivation ok?
Assumptions ok?
  Optical axis in sensor center?

## Slide 28
2d -> 3d Transformation
Parameters:
  sw
  sh
  pw= image width (pixels)
  ph= image height (pixels)
  f = focal length (m)
Open questions:
Video metadata often lacks sensor and focal parameters
Focal length can change during shooting (zooming)

## Slide 29
2d -> 3d Transformation
Experiment 1 in the wild (locations)
Nikon D800E:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  h = object height (m) = 1.5 m
  f = focal length (m) = 0.020 m
  fov = = 83.81 ⁰
Different locations and heights

## Slide 30
2d -> 3d Transformation
Experiment 2 in the wild (moving car)
Nikon D800E:
  sw = 0.0359 m
  sh
  pw= image width (pixels) = 7360
  ph= image height (pixels) = 4912
  h = object height (m) = 1.5 m
  f = focal length (m) = 0.050 m
  fov = = 39.49 ⁰
Car speeds:
  0
  20 km/h
  40 km/h
  60 km/h
  80 km/h
Distances:
  10 m
  20 m
  30 m
  40 m
  50 m
  60 m
  70 m
  80 m
  90 m
  100 m

## Slide 31
Map Presentation
z
x
image x - coordinate
image y – coordinate
field of view
object
observer
xw
zw
xi
yi
hw= image area world height (m)
hi = image area image height (pixels)
ww= image area world width (m)
wi = image area image width (pixels)
(xi, yi) = ( w* , * )
= = p (pixel/meter ratio)
(xi, yi) = ( w* , *p)

## Slide 32
Map Presentation
z
x
image x - coordinate
image y – coordinate
field of view
object
observer
sw
f = focal length (m)

## Slide 33
Map Presentation

## Slide 34
Entity Diagram
Detected Object
Image Object
Aero-
plane
Bicycle
Boat
Bottle
Bus
Car
Cat
Chair
Cow
Dining Table
Dog
Potted Plant
Person
Motor bike
Horse
Bird
TV
Monitor
Train
Sofa
Sheep
Event
Image World
Before

## Slide 35
Entity Diagram
V2.0 goal
Detected classes not hardcoded
Object class may change
Support for many cameras , rotations
Names less awkward
Cleaning
Python style guide followed, excluding line length
Code optimization
One package
Name of the software package: ShadowWorld
(Plato: Allegory of the Cave)

## Slide 36
Entity Diagram
Detection
Pattern
Event
World
V2.0
Camera
Body
”WorldObject”
”ImageObject”
”DetectedObject”
Trace
Speech
Synthesizer
Presentation3D
Presentation
…
PresentationMap
Bounding
Box
PresentationLog
Forecast

## Slide 37
Body Kalman Filtering
Second order model does not work, constant acceleration makes bodies bounce back or get enormous velocities.
In world, constant acceleration for several (tens) of seconds is not common
First order model works! (No wonder it’s popular in robotics…)
When measurement is lost, the body is switched into constant velocity mode
In filtering terminology: velocity mode = only prediction, no correction
Algorithms described in [docs] folder documents

## Slide 38
Body Kalman Filtering

## Slide 39
Body Kalman Filtering

## Slide 40
Body Kalman Filtering
Example: Car

## Slide 41
Body Kalman Filtering
Measurement status: 1=measurement
0=no measurement

## Slide 42
Body Kalman Filtering

## Slide 43
Body Kalman Filtering

## Slide 44
Body Kalman Filtering

## Slide 45
Body Kalman Filtering

## Slide 46
Body Kalman Filtering
Example 2: Slow moving object

## Slide 47
Body Kalman Filtering
Takes long time to settle

## Slide 48
Body Kalman Filtering

## Slide 49
Body Kalman Filtering

## Slide 50
Body Kalman Filtering
Filtering requires several seconds to achieve reliable results
Kalman filter parameters are not optimized
Optimization will be done later

## Slide 51
Paper
Contents:
Abstract
Introduction
Related work
Our approach
  Definitions
  Object identity
  Distance estimation
  Location and velocity estimation
  Movement prediction
Experiments
  Test setup
  Evaluation metric
  Results
  Other experiments
Conclusion
Image-based situation awareness: Estimating location and velocity using single camera object detection
?????
detection, pattern…
Hungarian algorithm, distance metrics,
movement prediction
geometry
Kalman filtering
Difference equation, uncertanties
In the wild. See previous slides. More?
Existing datasets? Which?

## Slide 52
Paper
One solution for location estimation and movement prediction for video detected object (nearly) solved
Work needed:
  Kalman filter parameter adjustment*
  Experiments in the wild (see previous slides)
  Other tests? (using existing (tracking) dataset)
Where to publish?
  ECCV 2018 (8-14.9, Munich, deadline 14.3.2018, too soon)
  CVPR 2019 (6/2019, Long Beach, deadline 11/2018)
  ICCV 2019 (29.10.-3.11.2019, Seoul, deadline 1/2019)
*Locations and especially velocities take too much time to settle at the moment.

## Slide 53
Representations for Interpretation
Object detection network
Location and velocity estimation
Forecast
Representation: Video
Representation: Body
Representation: Pattern
Representation: Time series
Interpretation Generation
I1
I2
I3
…
Interpretation representations
Language Generation

## Slide 54
Representations for Interpretation
Example for interpretation representation: collision detection
Time series forecast for body locations
Interpretation Generation
(Symmetric) collision probability matrix
pnm = probability that bodies n and m will collide

## Slide 55
Probabilistic Model for Body
Some form of spatial simplification is needed, like
cube
rectangular prism
cylinder
sphere (probably the easiest math)
x
z
y
rc
From state estimation
Class specific, a priori
s

## Slide 56
Collision Detection
si
sj
dij
rj
ri
Collision Cij if dij < ri + rj
Random variable
t: uniform distribution on [0, tend]
Sampling:
Open question: More efficient sampling with MCMC / Metropolis-Hastings?

## Slide 57
Collision Detection
x
z
y
rc
s
Collision with the observer (body ”0”)
S=[0,0,0,0,0,0]T , deterministic, r = r[class person]

## Slide 58
Collision Detection
Side effect: instead of using height in distance estimation,
radius of surrounding circle will be used:
h
w
r
α
From bounding box coordinates to radius:
tan(α)
cos(α)
/2

## Slide 59
Collision Detection
Distance estimation using object radius:
sw
sh
pw= image width (pixels)
ph= image height (pixels)
hi = object height (pixels)
h = object height (m)
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
sw
sh
pw= image width (pixels)
ph= image height (pixels)
ri = object radius (pixels)
r = object radius (m)
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
Before
Now

## Slide 60
Collision Detection
Distance estimation using object radius:
(xc, yc, zc) = (- * , * , -f)
(xo, yo, zo) = t* (xc, yc, zc)

## Slide 61: Work in Progress

## Slide 62
Perception
“The first step in achieving SA is to perceive the status, attributes, and dynamics of relevant elements in the environment. Thus, Level 1 SA, the most basic level of SA, involves the processes of monitoring, cue detection, and simple recognition, which lead to an awareness of multiple situational elements (objects, events, people, systems, environmental factors) and their current states (locations, conditions, modes, actions).”

## Slide 63: Next Steps

## Slide 64
Next steps
Comprehension:
Closing the open questions
2d -> 3d transformation
World object state estimation

## Slide 65: To Be Discussed

## Slide 66
To Be Discussed
Activity recognition?
Emotion recognition?
Turning camera, estimation by background movement?

## Slide 67: Thank you!
lampola@student.tut.fi
https://github.com/SakariLampola/Thesis