## Slide 1: Image-Based Situation Awareness Audit 8.5.2018
Sakari Lampola

## Slide 2: Previous Audit 28.2.2018

## Slide 3
Next steps
Kalman filter parameter adjustments (Q1)
Dataset selection (Q1)
Stereo vision (Q2)
Camera yaw, pitch, roll estimation (Q2)
Speech recognition (Q2)
Semantic segmentation (Q2)
Experiments in the wild (Q2)
Paper (Q3)
Speech analysis (Q3)
Speech generation (Q3)
Use cases (Q4)
Other
Body forecast
  kinetic
  based on class history
  based on swarm history
R matrix estimation
Monograph or papers

## Slide 4: Project Plan

## Slide 5
Methodology / Preparation of research infra
  Software platforms are constructed and tested
  Off-the-shelf models are acquired and tested
  Necessary skills on platforms are learned
Methodology / Method survey
  Current state-of-art methods are studied
  Methods are constructed and tested on the software platforms
Method follow-up
  Screening of conference papers related to the subject
  Possibly integrating new methods to the project

## Slide 6: Work Done

## Slide 7
Dataset Selection
Specification:
  Video
  Stereo
  Distance information
  Outdoor + indoor
  Odometry
Open question: Indoor? Self generated?

## Slide 8
Image format / cropping
sw = sensor pixel width = 1392
sh = sensor pixel height = 512
iw = image pixel width
ih = image pixel height
Assumptions:
image is symmetrically cropped (optical center fixed)
rectification ignored
xi,yi

## Slide 9
https://github.com/tensorflow/models/tree/master/research/object_detection

## Slide 10
Lottery prize!!!! Will be used to implement localization and velocity estimation
One of these will be the final model.

## Slide 12
Stereo Vision
Left
Right
disparity d

## Slide 14
Mapping left and right image patterns
Pattern features to match
hue0
hue2
hue1
x,y = bounding box center location
saturation,value = mean values
3-bin hue histogram:

## Slide 15
Pattern matching based on feature difference is required!

## Slide 16
Probabilistic model answering the question: What is the probability two patterns represent the same object?
Feature vector F:
confidence
x
y
width
heigth
hue0
hue1
hue2
saruration
value
Note: Class is not included as it is required to be the same
Assumption:
P(i and j are same pattern) ~ N(Fi – Fj ∣ μF , VF)

## Slide 17
μF , VF were estimated by matching 84 patterns in 28 KITTI stereo image pairs representing city, residential, campus and
person categories, including both cars and pedestrians.
Note: Mean disparity (dX) is appr. 30 pixels

## Slide 20
Pattern matching is done using Hungarian algorithm with the distance metrics:
dij = -log(P(i and j are same pattern)) = -log(N(Fi – Fj ∣ μF , VF) )
If the probability that the patterns are same is near 1, the distance will be near zero. As the probability
decreases, the distance increases. The log is required to compare small numbers without numerical issues.

## Slide 21
Simple example

## Slide 23
Complicated example

## Slide 26: Too complicated!!! Curse of dimensionality makes probabilities (even with log) too small.
Simpler solution:
Left camera pattern
Right camera detection
wl
wh
xl,yl
wr
wr
xr,yl
STEREO_MATCHING_HORIZONTAL = 0.4
Hungarian algorithm for matching.
Note: Patterns are not generated for the right camera. Patterns life spans in two cameras lead to complications.

## Slide 27
Not perfect, but good enough for the moment.
Research topic for 2019

## Slide 28
After implementing stereo vision, we have two distance estimates:
  Distance based on stereo vision. Accurate in short distances (for Kitti, 20 meters)
  Distance based on size. Can be used in long distances where stereo vision is inaccurate.
f
A
B
C
D
E
h
hi
α
F
G
d =AF
sh
ph= image height (pixels)
ri = pattern radius (pixels)
r = body radius (m), mean from class specific distribution
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
sw
pw= image width (pixels)
f = focal length (m)
b = base line (m)
ds = disparity (pixels)
= altitude (rad)
β = azimuth (rad)

## Slide 29
Combining distance estimates:
stereo_max_distance = 20.0
Procedure is iterated until convergence or max_iter (or just used once?)
Initialization:

## Slide 30
Estimating disparity using matched patterns
Left camera pattern:
  x_min_left
  x_max_left
Right camera pattern:
  x_min_right
  x_max_right
0.5 * (x_min_left+x_max_left)-0.5*(x_min_right+x_max_right)

## Slide 31
x
z
y
xb,yb,zb = body center point
xp,yp,zp = pattern center point
3D projection
(xb, yb, zb) = t* (xp, yp, zp)
Where:
(xp, yp, zp) = (- * , * , -f)
sw
sh
pw= image width (pixels)
ph= image height (pixels)
f = focal length (m)
px = pattern center point location (x, pixels)
py = pattern center point location (y, pixels)
Note! Only left image used. Right image is used only for disparity calculation (in the context of distance estimation and 3D projection).

## Slide 33
Localizations follows Velodyne cloud pretty well!

## Slide 34
Current overall matching algorithm:
For left camera:
  Create detections
  Predict pattern locations
  Match detections to patterns
  For each unmatched detection
    Create pattern
    Create body
For right camera:
  Create detections
Match right camera detections to left camera patterns
Predict body locations
Create location measurements based on size and stereo
Correct body locations
Note: Pattern and body removals are not described.

## Slide 35
Kalman Filter Parameter Adjustments
Two levels of filtering:
  Pattern
    Pattern movement estimation for missing detections
  Body
    Coordinate and velocity estimation

## Slide 36
Detection
Pattern
Body
x_min
x_max
y_min
y_max
K1
K1
K1
K1
Left
x_min
x_max
y_min
y_max
Right
Distance estimation + 3D projection
K2
x_min’ vx_min’
x_max’ vx_max’
y_min’ vy_min’
y_max’ vy_max’
Camera parameters
x
y
z
x’
y’
z’
vx’
vy’
vz’

## Slide 37
Before
After

## Slide 38
PATTERN_ALFA
2*std = 20px, first detection bounding box accuracy
PATTERN_BETA
2*std = 200 px/s = 20 px / frame
PATTERN_Q
2*std = 20px, detection accuracy
PATTERN_R
Location, no teleporting
Velocity, 2*std = 20px/frame = 200 px/s
BODY_ALFA
2*std = 6 m, first location accuracy
BODY_BETA
2*std = 20 m/s
BODY_Q
2*std = 10m, measurement accuracy
BODY_R
Location, no teleporting
Velocity (x,z), 2*std = 2 m/s2
Velocity (y), 2*std = 0,6 m/s2

## Slide 39
Pattern location / before
Pattern location / after

## Slide 40
Pattern velocity / before
Pattern location / after

## Slide 41
Body location / before
Body location / after

## Slide 42
Body location / before
Body location / after

## Slide 43
Body Volume and Orientation
Bounding sphere is not a good shape for volumes like car, human or train…
KITTI uses bounded 3D box

## Slide 44
length
height
width
velocity = (vx,vy,vz)
Assumption: Only yaw allowed
y
x
z
p
p1
p4
p3
p5
p6
p7
p8
p2
Each body is supposed to have “normal” movement direction, which defines length, height and width.
α = yaw angle
α
…

## Slide 45
x
z
α
p’1
p2
p’5
p’6
p
n
v
a
b
p1
p’2
p6
p5
Top view
= *
Side view
x
y
y’1
y’2
x’1
x’2

## Slide 46
Currently used for display. Collision detection still uses spheres. TBD

## Slide 47
Grid and Body Forecast
Background:
Representing body forecast and probabilities in continuous world is presumably much more difficult than is discrete space. Grid is needed…

## Slide 48
2D grid is used, even spacing GRID_COUNT parameter (31)

## Slide 49
Representing conditional path statistics and probabilities is easier. Appropriate grid size?

## Slide 50
Open questions:
  Data? (KITTI Campus?)
  How to combine different probabilities (kinetic and stat based)?

## Slide 51
World Coordinates, Yaw, Pitch and Roll
y
x
z
Assumptions:
  initially world coordinates coincide with left camera
  y, roll and pitch are fixed
  x and z are estimated from odometry (GPS)
  yaw is estimated from optical flow
Camera has three degrees of freedom:
  x
  z
  yaw

## Slide 52
Transformation from (left) camera coordinates into world coordinates:
(Szeliski)
c from odometry
R from optical flow

## Slide 53
Frame n
Frame n+1
dx
From optical flow to yaw

## Slide 54
Approximation for small turns:
α
β
x1
x2
f
sensor plane
Substituting α=0 (reference):

## Slide 55
Cumulative yaw is maintained for the reference (left) camera:
sw
pw= image width (pixels)
f = focal length (m)
dxp = horizontal optical flow in pxels
Note: Approximation and optical flow errors are cumulative over time. However, the major effect of error is that the initial reference coordinate system is turning in space around y-axis. As this is completely arbitrary, it doesn’t matter much. If we would like to map environment, it would matter more.

## Slide 56
If more degrees of freedom are wanted:
So, quaternions, but later when needed…
(Szeliski)

## Slide 57
Calculating (dense) optical flow
Car turning left

## Slide 58
Horizontal dense optical flow calculated using Gunner Farneback’s algorithm. Hotter colour = more flow

## Slide 59
Distribution of horizontal flow values
Objects moving in opposite direction?
Areas without high fequency details
Usable area
Ad hoc algorithm to determine ’average’ background optical flow:
  Determine main direction (+/-)by calculating mean of flows
  Drop all flows in the opposite direction
  Calculate mean value of flows in right direction
  Drop all flows whose absolute value is below mean value
  Determine the final value by calculating mean value of remaining flows

## Slide 60: Next Steps

## Slide 61: Discussion

## Slide 62: Thank you!
lampola@student.tut.fi
https://github.com/SakariLampola/Thesis