## Slide 1: Image-Based Situation Awareness Audit 8.5.2018
Sakari Lampola

## Slide 2: Previous Audit 28.2.2018

## Slide 3
Next steps
Kalman filter parameter adjustments (Q1)
Dataset selection (Q1)
Stereo vision (Q2)
Camera yaw, pitch, roll estimation (Q2)
Speech recognition (Q2)
Semantic segmentation (Q2)
Experiments in the wild (Q2)
Paper (Q3)
Speech analysis (Q3)
Speech generation (Q3)
Use cases (Q4)
Other
Body forecast
  kinetic
  based on class history
  based on swarm history
R matrix estimation
Monograph or papers?

## Slide 4: Project Plan

## Slide 5
Methodology / Preparation of research infra
  Software platforms are constructed and tested
  Off-the-shelf models are acquired and tested
  Necessary skills on platforms are learned
Methodology / Method survey
  Current state-of-art methods are studied
  Methods are constructed and tested on the software platforms
Method follow-up
  Screening of conference papers related to the subject
  Possibly integrating new methods to the project

## Slide 6: Work Done

## Slide 7
Dataset Selection
Specification:
  Video
  Stereo
  Distance information
  Outdoor + indoor
  Odometry
Open question: Indoor? Self generated?

## Slide 8
Image format / cropping
sw = sensor pixel width = 1392
sh = sensor pixel height = 512
iw = image pixel width
ih = image pixel height
Assumptions:
image is symmetrically cropped (optical center fixed)
rectification ignored
xi,yi

## Slide 9
https://github.com/tensorflow/models/tree/master/research/object_detection

## Slide 10
Lottery prize!!!! Will be used to implement localization and velocity estimation
One of these will be the final model.

## Slide 12
Stereo Vision
Left
Right
disparity d

## Slide 14
Mapping left and right image patterns
Pattern features to match
hue0
hue2
hue1
x,y = bounding box center location
saturation,value = mean values
3-bin hue histogram:

## Slide 15
Pattern matching based on feature difference is required!

## Slide 16
Probabilistic model, answering the question: What is the probability two patterns represent the same object?
Feature vector F:
confidence
x
y
width
heigth
hue0
hue1
hue2
saruration
value
Note: Class is not included as it is required to be the same
Assumption:
P(i and j are same pattern) ~ N(Fi – Fj ∣ μF , VF)

## Slide 17
μF , VF were estimated by matching 84 patterns in 28 KITTI stereo image pairs representing city, residential, campus and
person categories, including both cars and pedestrians.
Note: Mean disparity (dX) is appr. 30 pixels

## Slide 20
Pattern matching is done using Hungarian algorithm with the distance metrics:
dij = -log(P(i and j are same pattern)) = -log(N(Fi – Fj ∣ μF , VF) )
If the probability that the patterns are same is near 1, the distance will be near zero. As the probability
decreases, the distance increases. The log is required to compare small numbers without numerical issues.

## Slide 21
Simple example

## Slide 23
Complicated example

## Slide 26: Too complicated!!! Curse of dimensionality makes probabilities (even with log) too small.
Simpler solution:
Left camera pattern
Right camera detection
wl
wh
xl,yl
wr
wr
xr,yl
STEREO_MATCHING_HORIZONTAL = 0.4
Hungarian algorithm for matching.
Note: Patterns are not generated for the right camera. Patterns life spans in two cameras lead to complications.

## Slide 27
Not perfect, but good enough for the moment.
Research topic for 2019

## Slide 28
After implementing stereo vision, we have two distance estimates:
  Distance based on stereo vision. Accurate in short distances (for Kitti, 20 meters)
  Distance based on size. Can be used in long distances where stereo vision is inaccurate.
f
A
B
C
D
E
h
hi
α
F
G
d =AF
sh
ph= image height (pixels)
ri = pattern radius (pixels)
r = body radius (m), mean from class specific distribution
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
sw
pw= image width (pixels)
f = focal length (m)
b = base line (m)
ds = disparity (pixels)
= altitude (rad)
β = azimuth (rad)

## Slide 29
Combining distance estimates:
stereo_max_distance = 20.0
Procedure is iterated until convergence or max_iter (or just used once?)
Initialization:

## Slide 30
Estimating disparity using matched patterns
Left camera pattern:
  x_min_left
  x_max_left
Right camera pattern:
  x_min_right
  x_max_right
0.5 * (x_min_left+x_max_left)-0.5*(x_min_right+x_max_right)

## Slide 31
x
z
y
xb,yb,zb = body center point
xp,yp,zp = pattern center point
3D projection
(xb, yb, zb) = t* (xp, yp, zp)
Where:
(xp, yp, zp) = (- * , * , -f)
sw
sh
pw= image width (pixels)
ph= image height (pixels)
f = focal length (m)
px = pattern center point location (x, pixels)
py = pattern center point location (y, pixels)
Note! Only left image used. Right image is used only for disparity calculation (in the context of distance estimation and 3D projection).

## Slide 33
Localizations follows Velodyne cloud pretty well!

## Slide 34
Current overall matching algorithm:
For left camera:
  Create detections
  Predict pattern locations
  Match detections to patterns
  For each unmatched detection
    Create pattern
    Create body
For right camera:
  Create detections
Match right camera detections to left camera patterns
Predict body locations
Create location measurements based on size and stereo
Correct body locations
Note: Pattern and body removals are not described.

## Slide 35
Research topic!
The joint estimation of pattern and body state would be a good area for further study. The current algorithm is by no means optimal.

## Slide 36
Kalman Filter Parameter Adjustments
Two levels of filtering:
  Pattern
    Pattern movement estimation for missing detections
  Body
    Coordinate and velocity estimation

## Slide 37
Detection
Pattern
Body
x_min
x_max
y_min
y_max
K1
K1
K1
K1
Left
x_min
x_max
y_min
y_max
Right
Distance estimation + 3D projection
K2
x_min’ vx_min’
x_max’ vx_max’
y_min’ vy_min’
y_max’ vy_max’
Camera parameters
x
y
z
x’
y’
z’
vx’
vy’
vz’

## Slide 38
Before
After

## Slide 39
PATTERN_ALFA
2*std = 20px, first detection bounding box accuracy
PATTERN_BETA
2*std = 200 px/s = 20 px / frame
PATTERN_Q
2*std = 20px, detection accuracy
PATTERN_R
Location, no teleporting
Velocity, 2*std = 20px/frame = 200 px/s
BODY_ALFA
2*std = 6 m, first location accuracy
BODY_BETA
2*std = 20 m/s
BODY_Q
2*std = 10m, measurement accuracy
BODY_R
Location, no teleporting
Velocity (x,z), 2*std = 2 m/s2
Velocity (y), 2*std = 0,6 m/s2

## Slide 40
Pattern location / before
Pattern location / after

## Slide 41
Pattern velocity / before
Pattern location / after

## Slide 42
Body location / before
Body location / after

## Slide 43
Body location / before
Body location / after

## Slide 44
Research topic!
Note. The current filter architecture and parameters do their job, but certainly are
not optimal. Field for further study!

## Slide 45
Body Volume and Orientation
Bounding sphere is not a good shape for volumes like car, human or train…
KITTI uses bounded 3D box

## Slide 46
length
height
width
velocity = (vx,vy,vz)
Assumption: Only yaw allowed
y
x
z
p
p1
p4
p3
p5
p6
p7
p8
p2
Each body is supposed to have “normal” movement direction, which defines length, height and width.
α = yaw angle
α
…

## Slide 47
x
z
α
p’1
p2
p’5
p’6
p
n
v
a
b
p1
p’2
p6
p5
Top view
= *
Side view
x
y
y’1
y’2
x’1
x’2

## Slide 48
Currently used for display. Collision detection still uses spheres. TBD

## Slide 49
Grid Representation
Background:
Representing body movement forecast and probabilities in continuous world is presumably much more difficult than in discrete space. Grid is needed…

## Slide 50
2D grid is used, with evenly spaced lines. GRID_COUNT parameter (=31)

## Slide 51
Representing conditional path statistics and probabilities is easier with grid.

## Slide 52
Note. KITTI dataset includes ”Person” category wich is well suited to do research.
Research topic!
Nearly 100 videos where one or more persons are walking using different paths across the same area.

## Slide 53
World Coordinates, Yaw Estimation
y
x
z
Assumptions:
  initially world coordinates coincide with left camera
  y, roll and pitch are fixed
  x and z are estimated from odometry (GPS)
  yaw is estimated from optical flow, or given
Camera has three degrees of freedom:
  x
  z
  yaw

## Slide 54
Transformation from (left) camera coordinates into world coordinates:
(Szeliski)
c from odometry
R from optical flow

## Slide 55
x
z
x’
z’
yaw
camera
body
xb’,zb’
xc,zc
From camera coordinates into world coordinates:
world coordinates (initial camera location)
)
From world coordinates into camera coordinates:

## Slide 56
If more degrees of freedom are wanted:
So, quaternions, but later when needed…
(Szeliski)

## Slide 57
Car going straight ahead. Optical flow to left is coloured blue,
and flow to right red. It is calculated using Farneback algorithm.

## Slide 58
Car turning left. Optical flow is mainly to right and colored red/yellow.

## Slide 59
Frame n
Frame n+1
dx
From optical flow to yaw

## Slide 60
Approximation for small turns:
α
β
x1
x2
f
sensor plane
Substituting α=0 (reference):

## Slide 61
Cumulative yaw is maintained for the reference (left) camera:
sw
pw= image width (pixels)
f = focal length (m)
dxp = horizontal optical flow in pxels
Note: Approximation and optical flow errors are cumulative over time. However, the major effect of error is that the initial reference coordinate system is turning in space around y-axis. As this is completely arbitrary, it doesn’t matter much. If we would like to map environment, it would matter more.

## Slide 62
Distribution of horizontal flow values
Objects moving in opposite direction?
Areas without high fequency details
Usable area
Ad hoc algorithm to determine ’average’ background optical flow:
  Determine main direction (+/-) by calculating mean of flows
  Drop all flows in the opposite direction
  Calculate mean value of flows in right direction
  Drop all flows whose absolute value is below mean value
  Determine the final value by calculating mean value of remaining flows

## Slide 63
Naive ad hoc algorithm is not very good, but a starting point…

## Slide 64
Note 1. Lucas-Kanade algorithm is another possibility. It concentrades on areas with texture and high frequency details. Anyway, areas corresponding to patterns should be eliminated.
Note 2. KITTI dataset includes 6 DOF data for moving camera. Lots of data to do research!!!
Research topic!

## Slide 65
COCO Dataset
Why?
171 everyday common categories
Large amount of images
Good API
Emerging support for implementations
Captions
Common Objects in Context

## Slide 66
COCO things (=bodies)

## Slide 67
COCO stuff

## Slide 68
ShadowWorld 4.0 user interface for COCO (with faster rcnn/resnet101 object detection network):

## Slide 69
Semantic Segmentation
Why?
The goal is to give rich view description. For that, we need
the bodies (things) and context (stuff).

## Slide 70
Unfortenately, there is no TensorFlow implementation for COCO stuff detection. However, there are Caffe
implementations. For those implementations, necessary files for converting them into OpenCV DNN
could not be found.
Options to continue:
  Wait until TensorFlow implementation is available.
  Learn Caffe and export an implementation into TensorFlow (or construct a bridge from Caffe to TensorFlow).
  Take existing TensorFlow implementation (for example DeepLab/Pascal VOC 2012) and use transfer learning to adapt into COCO.
  Teach a TensorFlow network from scratch.
I chose to wait until July 2018. If there is no TensorFlow implementation at that time, option 2 is followed. If that fails, option 3 is taken. Option 4 would be very tempting, with a lot to learn. However, there are so many moving parts and hyperparameter adjustments in the process, that this time option 4 should be avoided. If it were followed, it would be a great research topic. It would also require using cloud services, which are not free.
Data is available.

## Slide 71
Until having a semantic segmentation implementation, the COCO ground
truth will be used to develop natural
language models.
To summarize:
Things are created by object detection, stuff
using semantic segmentation.

## Slide 72
Speech Recognition
SpeechRecognition 3.8.1 Python package
+
PocketSphinx
Google API Client Library for Python +
Google Cloud Speech API much more better, but not free.
Will be used in the prototype. Requires network connection.

## Slide 73
Use Cases

## Slide 75
OCR
Attribute extraction
Requires specific network
Impossible?
Research topic!

## Slide 76
Note: Because VizWiz is based on q/a data on
specific mobile app, some questions are
absent, probably because people know it is
unable to give the answer. Most notably,
questions beginning ”where”. This is where
image based situation awereness shines!
But it also means that we cannot use pure
VizWiz as learning and evaluation dataset.
Another set of questions having only small
number of representatives is ”How many…?”
The goal will be to cover large amount
of this this circle + some extra questions.

## Slide 77
ShadowWorld integration (easy example, more behind the link on Youtube video…)

## Slide 78
Dataset Roles
KITTI
  3D object localization
  State estimation
  Forecasting
COCO
  Object and stuff classes
  Network implementations
VIZWIZ
  Use cases

## Slide 79
New Ideas
Using masks instead of (or with) bounding boxes:
Mask can be applied to conventional stereo disparity map to get
many distance measurements. Object attributes more accurate.

## Slide 80
Current network
Mask networks
TensorFlow Object Detection Model Zoo

## Slide 81
Particle cloud representation for both things (bodies) and stuff
  Volumes
  Helps probabilistic reasoning
Grid (2D or 3D) world representation
  Enables set of methods and tools developed for grid representation

## Slide 82: Next Steps

## Slide 83: Discussion

## Slide 84: Thank you!
lampola@student.tut.fi
https://github.com/SakariLampola/Thesis