## Slide 1: Image-Based Situation Awareness Audit 8.5.2018
Sakari Lampola

## Slide 2: Previous Audit 28.2.2018

## Slide 3
Next steps
Kalman filter parameter adjustments (Q1)
Dataset selection (Q1)
Stereo vision (Q2)
Camera yaw, pitch, roll estimation (Q2)
Speech recognition (Q2)
Semantic segmentation (Q2)
Experiments in the wild (Q2)
Paper (Q3)
Speech analysis (Q3)
Speech generation (Q3)
Use cases (Q4)
Other
Body forecast
  kinetic
  based on class history
  based on swarm history
R matrix estimation
Monograph or papers

## Slide 4: Project Plan

## Slide 5
Methodology / Preparation of research infra
  Software platforms are constructed and tested
  Off-the-shelf models are acquired and tested
  Necessary skills on platforms are learned
Methodology / Method survey
  Current state-of-art methods are studied
  Methods are constructed and tested on the software platforms
Method follow-up
  Screening of conference papers related to the subject
  Possibly integrating new methods to the project

## Slide 6: Work Done

## Slide 7
Dataset Selection
Specification:
  Video
  Stereo
  Distance information
  Outdoor + indoor
  Odometry
Open question: Indoor? Self generated?

## Slide 8
Image is resized to 300*300 pixels

## Slide 9
Resized KITTI image is too deformed to be useful. We need another network implementation!
https://github.com/tensorflow/models/tree/master/research/object_detection

## Slide 10
Lottery prize!!!! Will be used to implement localization and velocity estimation
One of these will be the final model.

## Slide 12
Stereo Vision
Left
Right
disparity d

## Slide 14
Mapping left and right image patterns
Pattern features to match
hue0
hue2
hue1
x,y = bounding box center location
saturation,value = mean values
3-bin hue histogram:

## Slide 15
Pattern matching based on feature difference is required!

## Slide 16
Probabilistic model answering the question: What is the probability two patterns represent the same object?
Feature vector F:
confidence
x
y
width
heigth
hue0
hue1
hue2
saruration
value
Note: Class is not included as it is required to be the same
Assumption:
P(i and j are same pattern) ~ N(Fi – Fj ∣ μF , VF)

## Slide 17
μF , VF were estimated by matching 84 patterns in 28 KITTI stereo image pairs representing city, residential, campus and
person categories, including both cars and pedestrians.
Note: Mean disparity (dX) is appr. 30 pixels

## Slide 20
Pattern matching is done using Hungarian algorithm with the distance metrics:
dij = -log(P(i and j are same pattern)) = -log(N(Fi – Fj ∣ μF , VF) )
If the probability that the patterns are same is near 1, the distance will be near zero. As the probability
decreases, the distance increases. The log is required to compare small numbers without numerical issues.

## Slide 21
Simple example

## Slide 23
Complicated example

## Slide 26
After implementing stereo vision, we have two distance estimates:
  Distance based on stereo vision. Accurate in short distances (for Kitti, 20 meters)
  Distance based on size. Can be used in long distances where stereo vision is inaccurate.
f
A
B
C
D
E
h
hi
α
F
G
d =AF
sh
ph= image height (pixels)
ri = pattern radius (pixels)
r = body radius (m), mean from class specific distribution
f = focal length (m)
= altitude (rad)
β = azimuth (rad)
sw
pw= image width (pixels)
f = focal length (m)
b = base line (m)
ds = disparity (pixels)
= altitude (rad)
β = azimuth (rad)

## Slide 27
Combining distance estimates:
stereo_max_distance = 20.0
Procedure is iterated until convergence or max_iter (or just used once?)
Initialization:

## Slide 28
Estimating disparity using matched patterns
Left camera pattern:
  x_min_left
  x_max_left
Right camera pattern:
  x_min_right
  x_max_right
0.5 * (x_min_left+x_max_left)-0.5*(x_min_right+x_max_right)

## Slide 29
x
z
y
xb,yb,zb = body center point
xp,yp,zp = pattern center point
3D projection
(xb, yb, zb) = t* (xp, yp, zp)
Where:
(xp, yp, zp) = (- * , * , -f)
sw
sh
pw= image width (pixels)
ph= image height (pixels)
f = focal length (m)
px = pattern center point location (x, pixels)
py = pattern center point location (y, pixels)
Note! Only left image used. Right image is used only for disparity calculation (in the context of distance estimation and 3D projection).

## Slide 30
Kalman Filter Parameter Adjustments
https://github.com/kcg2015/Vehicle-Detection-and-Tracking

## Slide 31
Kalman Filter Parameter Adjustments

## Slide 32
Kalman Filter Parameter Adjustments

## Slide 33
Kalman Filter Parameter Adjustments

## Slide 34: The Big Picture

## Slide 35
Visual Analysis
Speech Recognition
Bodies (+attributes)
Context
Forecasts
Collision probabilities
Other representations
Speech Generation
Words per minute: max 150…160
Priority queue, active dropping
CNN + Object Detection
Speech Analysis
Commands Questions
Semantic Segmentation
Matching
Pattern filtering
Distance estimation
3D projection
Body filtering
Body prediction
Collision detection
…
Syntactic classification
Semantic classification
Speech Synthesis
Generated based on situation:
Commands:
Q/A: (Answer voice: NOTICE)
High female
Low female
High male
Low male
Voice
Stereo Vision

## Slide 36: Next Steps

## Slide 37
Next steps
Kalman filter parameter adjustments (Q1)
Dataset selection (Q1)
Stereo vision (Q2)
Camera yaw, pitch, roll estimation (Q2)
Speech recognition (Q2)
Semantic segmentation (Q2)
Experiments in the wild (Q2)
Paper (Q3)
Speech analysis (Q3)
Speech generation (Q3)
Use cases (Q4)

## Slide 38: Discussion

## Slide 39: Thank you!
lampola@student.tut.fi
https://github.com/SakariLampola/Thesis